## Slide 1: Modular Wireless Xbox Kinect Data Transfer Device (MWXKDTD)
Team: ECE 409
Millad Nooristani, Eric Olson, Ayush Rohatgi

## Slide 2: Project Description
This project to allow several Xbox Kinects to connect and transmit to a host system simultaneously
This is useful for two reasons:
  It gives wireless functionality to the Xbox Kinect with Windows 10
  It allows several Kinects to work on the same system, which is not doable through USB hardwire connection
This will most likely be used for research purposes
  This is the main use of all Xbox Kinects currently
This allows multi-Kinect systems to be more spread out and to function on the same system without the installation of extra PCI cards

## Slide 3: Requirements
Main Requirements:
  Host a steady stream of Kinect data to be displayed on a host system
  Allow for multiple streams simultaneously
  Integrate with existing Kinect projects
Sub-Requirements:
  The addition of multiple streams does not impact the quality of existing streams
  Able to switch between data type streams at user command
  User-friendly Windows interface

## Slide 4: System Overview: Conceptual Functional diagram

## Slide 5: System Overview: Major Functions/Subsystems
Major Functions
  Kinect data capturing
    Performed on Raspberry Pi
    Uses installed libraries Libfreenect and OpenCV
    Sends data using SSH Wi-Fi connection protocol over a closed network
  Host System Display
    Still in development
    Will most likely be through Matlab or created GUI

## Slide 6: Design and Justification: Conception
Self created idea
  Only constraint was to use a Raspberry Pi and a Kinect
Earlier ideas
  Wired Kinect Hub for multiple Kinects on one PCI card
    Too many Pis to make economic sense
  Bluetooth Xbox Kinect Data Transfer Device
    Bluetooth proved slow and annoying to use

## Slide 7: Design and Justification: Current
Modular Wireless Xbox Kinect Data Transfer Device
  The switch to using a Wi-Fi network accomplished many things:
    Cheaper than original wired hub (one less Pi required)
    Limited data loss as compared to Bluetooth
      Even more relevant when supporting multiple cameras
    Larger range
      Easier to extend Wi-Fi network range than to extend Bluetooth network range

## Slide 8: Implementation of Design: Functions
HW
  Pi and Host Computer
    Wireless communication through SSH Wi-Fi protocol
  Xbox Kinect
    RGB and Depth Image capture
SW
  Pi
    Python scripting
    Data capturing, parsing, and forwarding to host system
  Host (Windows System)
    Data receiving
    User Friendly data display and data type options
    User ability to activate/deactivate individual cameras on the network

## Slide 9: Implementation of Design: I/0
Inputs
  Kinect -> Raspberry Pi -> Host
    RGB and Depth Image data
  Host -> Raspberry Pi
    User inputs: data types, activate/deactivate
Outputs
  Host
    RGB or Depth Image data

## Slide 10: Implementation of Design: Integration
  SW
    Kinect is a Windows product, and Pi is running Raspbian
      This is solved with the libraries Libfreenect and OpenCV
    Image data from the network to the host
      This is still in development
  I/O
    Kinect <-> Pi
      USB 2.0
    Pi <-> Network
      Wi-Fi
    Network <-> Host
      Ethernet

## Slide 11: Work Breakdown
Main Tasks
  Stream and display data from Pi to Host (in progress)
  Add multiple simultaneous streams from several Pis
  Do something with the stream (most likely legacy multi-Kinect facial recognition project)
Who is doing what
  Now: Stream and Pi-case
    Whole group
  Later: Multiple Streams and facial recognition
    Will split into teams

## Slide 13: Moving Forward
Currently
  We have isolated the data from the Kinect on the Raspberry Pi
  We need to find the most efficient way to transmit the data
  Slowest: We convert the data to image format on Pi and send
    Tested: 4-5 FPS with transmission
  Fastest: We don’t modify data at all on Raspberry Pi
    Tested: 30 FPS without transmission
    Problem: we need to find a way to process data on host system

## Slide 14: Moving Forward
Future
  Find way to process data on Host and display
    Possible ways
      Write a GUI from scratch and process data for display in real time
      Try to virtualize Kinect data for use with existing Matlab library